## Slide 1
MISSION DRIVEN: To Move the World at Work
CDRL E003 CFAT REPORT TEMPLATE
SUPPLIER TRAINING ON JLTV CFAT AND INSTRUCTIONS ON HOW TO COMPLETE THE E003 REPORT TEMPLATE

## Slide 2
Welcome to CFAT Training
Pay ATTENTION: You will be quizzed throughout this presentation

## Slide 3
Timing and Submission of Reports
Submitting Documents:
  All documents are submitted through the Oshkosh FTP site. DO NOT EMAIL!
Timing:
  Test reports must be submitted within 20 days of completion of a CFAT test.

## Slide 4: CDRL E003 CFAT Report: Page 1 (Cover)
A
B
C
D
E
F
G
Enter the part number exactly as listed on the drawing
Enter the revision level of the part.
Enter the part description as listed on the drawing
Enter your company name
Enter your supplier manufacturing cage code ID. If any third-party test facilities were utilized, please include these as well
Five digit alphanumeric code
https://cage.dla.mil/
Enter the PO number that was issued with CFAT testing language
Include the start and end dates on which testing occurred
Contract and Clin numbers should remain as they are on the template
Report numbers will be supplied to you by your CFAT coordinator
H
I

## Slide 5: CDRL E003 CFAT Report: Page 1 (Cover Example)

## Slide 6: CDRL E003 Report: Page 2
A
Insert the revision level (first 01), date, and initial revision for the first submission. If revisions or corrections need to be made, state the next revision (02, 03, etc…), date, and list revisions since the last submission.
Type the name of the supplier’s representative for CFAT activities.
Insert the representative’s title.
Signature of the supplier’s representative is required.
Insert the date the report is approved by the supplier.
B
C
D
E

## Slide 7: CDRL E003 Report: Page 4
Once the rest of the report is complete, please return to this page and ensure that the section titles and pages align with the rest of the report.

## Slide 8: CDRL E003 Report: Introduction, Page 5
Enter in your company name, PN as it is listed on the drawing, and revision level of the drawing.
1.2 Instructions:
  Enter the part description as entered on the drawing.
  Enter the National Stock Number of the part. If this is unknown, it has likely not been assigned, in which case this line can be filled out as N/A.
  Enter the PN and Revision Level as listed on the drawing.
  Include type of items tested.
  Enter the heat lot and/or serial numbers of the test samples here.
  Please list any approved ECPs associated with the PN here.
  The drawing can be referred back to here.
  Enter the Date(s) of manufacture for the test samples.
A
C
B
1.3 Instructions:
  Replace xxx with the part number.
  Replace xxx with part number and list the performance, durability, and environmental requirements from the drawing

## Slide 9: CDRL E003 Report: Page 5, Summary
A
B
C
Provide a summary of the tests performed along with the results.
Provide a description of any failures which occurred along with the associated corrective actions.
Describe any deviations from the CFAT plan. This may include any issues with test equipment or any minor deviations from the schedule.
Include a summary table of performance data results taken.
D

## Slide 10
Question 1:
How many days do you have to submit your CFAT Report?
Question 2:
What deviations from the CFAT plan must be noted in the Summary section?
Question 3:
How should CFAT reports be submitted?

## Slide 11
CDRL E003 Report: Page 6
This field only applies if prior CFAT testing has been conducted on the same part.
For the placeholders, use the part number and reference the date the E002 JPO approval notification was sent.
Any prior CFAT certifications for the PN would be referenced here. If there are none, this section should be completed as N/A.
Designate how and where CFAT records are being held.
List all standards used in CFAT testing as referenced in the drawing.
A
B
C
D
E

## Slide 12: CDRL E003 Report: Sections 4.1 and 4.2
Include a list of equipment used in testing. The table from the CFAT plan can be used for this, though if different equipment was used, any equipment not used from the plan should be removed from the list and replaced with the equipment actually used in CFAT.
Describe the equipment set-ups of the testing performed in CFAT. Pictures and/or illustrations of the test set-up may be included in an appendix, though accompanying verbiage describing the photos should be included.
A
B

## Slide 13: CDRL E003 Report: Sections 4.3 and 4.4
Describe the selection of the test samples.
Provide a summary of the testing that took place, which should include the sequence and a brief description of the test procedures.
Reference the section under which the data is provided in the report.
This field only applies if prior CFAT testing was conducted on this part.
Include any calculations that were used in the report.
Similar to section 2.0 C. in the Summary section, describe any anomalies or failures that occurred during testing.
A
B
C
D
E
F

## Slide 14: CDRL E003 Report: Sections 4.5 and 4.6
Provide for each subsection of sections 4.5 and 4.6 a brief statement addressing the success of the test, whether additional testing is required, etc.
CFAT Samples are to be retained through approval of the E003 by the JPO. Your CFAT coordinator will advise on how to properly disposition your samples.
A
B

## Slide 15: Lab Qualification Documentation
Documentation necessary for testing performed at a lab accredited to ISO 17025:
  Test results submitted in the normal laboratory report format.
  The laboratory’s accreditation standard, including the lab’s accreditation number and/or the name of the organization which provided the accreditation.
  List of standards used for testing.
  Date(s) on which testing took place.
  The name of the laboratory that performed the test.
Documentation necessary for testing performed at a facility not accredited to ISO 17025:
  The name of the laboratory that performed the test.
  Work instructions for each test conducted.
  Training records / certifications of personnel who performed the testing.
  List of all test equipment used to perform testing.
  Calibration records of all test equipment used.
  The date on which the testing took place

## Slide 16
Question 1:
What documentation is required for lab qualification?
Question 2:
What should be done with the tested samples upon completion of CFAT?
Question 3:
What information should you include in report section 4.5: Conclusions?

## Slide 17
CDRL E003 – MISC. NOTES
Upload the test report and supporting documentation to FTP – do not send through email.
Send an email to your AQE and CFAT coordinator to download and review.
The only PPAP Documentation that should be included is that which verifies the parts are in compliance with the other, general print notes of the drawing. MSA’s, Control Plans, PFMEA, DFMEA, and any other APQP documentation are not required to be included in the report, but will need to be included in your PPAP level 3. Some examples of necessary documentation for this would include material or paint certifications if they are referenced on the drawing.

## Slide 18: QUESTIONS ?